FOR IMMEDIATE RELEASE

## December 17, 2012

Headline: Robbins Main Beam will dig below Indianapolis

Sub-Headline: Hard Rock Heavyweight to carve out Midwest Water Tunnel

On November 27, 2012 a 6.2 m (20.2 ft) diameter Robbins hard rock cutterhead arrived in Indianapolis, Indiana, USA.  The arrival at the staging site was timed with a ceremony that included the city’s mayor and local officials, marking the assembly progress of the large Main Beam TBM.  Once launched from a 76 m (250 ft) deep shaft, the machine will embark on a 12.2 km (7.5 mi) long wastewater tunnel for the Shea/Kiewit JV.

The contractor-owned Robbins machine was refurbished and redesigned in Cleveland, Ohio and Mt. Pleasant, Pennsylvania facilities following its most recent excavation at New York City’s Second Avenue Subway.

Its latest rebuild was complex, according to Dave Girard, Senior Engineer for J.F. Shea Construction: “We retrofitted a machine built in 1976 with the latest technology--in particular, variable frequency drive motors.” Other new components include the back-loading cutterhead with 19-inch disc cutters and rescue chamber.

Despite the complexities of the redesign, the machine is scheduled to be launched from a deep shaft in early 2013, proceeding towards the Belmont Wastewater Treatment Plant in what is expected to be competent limestone and dolomite rock.  Robbins continuous conveyors, including a horizontal and vertical conveyor, will aid in muck removal on the long drive.

Once complete, the tunnel will be lined with un-reinforced concrete, making the finished diameter 5.5 m (18 ft).  Cleaner water is the ultimate goal of the city’s new Deep Rock Tunnel Connector (DRTC), along with four shorter tunnels that will be added on afterwards.  The DRTC will convey up to 2.1 million m3 (550 million gallons) of combined sewer overflows daily to the Southport Advanced Water Treatment Plant.   By 2025, the network of five tunnels will total over 40 km (25 mi), and will reduce wastewater overflow into the White River, Fall Creek, Pogues Run and Pleasant Run waterways by 95 percent or more.

WORD COUNT: 309

Images Attached to Email.  If you need a higher resolution image, please contact Desiree Willis.

Captions for Images:

Image 1: A Robbins Main Beam TBM is preparing to excavate the Indianapolis DRT for JV contractor Shea/Kiewit.

Image 2: The contractor-owned machine includes a cutterhead refurbished by Robbins, with 19-inch disc cutters.

Contact Information:

## Brianna Home

#### Marketing Director

### Email: homeb@robbinstbm.com

Direct: 253.872.4484

## Desiree Willis

#### Technical Writer

Email: willisd@robbinstbm.com

Direct: 253.872.4490

##### The Robbins Company

29100 Hall Street

Solon, OH 44139

USA