New DT912D delivers intelligent efficiency in underground mineral excavation

Sandvik Construction is introducing a completely new tunneling jumbo to its extensive offering, the DT912D. Designed especially for limestone applications, this new high reach - single boom jumbo is completely self-contained, powered by a fuel efficient and environmentally friendly Tier 4 Final diesel engine. It is also equipped with an onboard compressor and water-tank for air-mist flushing. With the new, intelligent, state-of-the-art control system, it brings to customers high quality operations and increased productivity in both tunneling and underground mine production.

The DT912D – a self-contained, air-mist flushing, diesel-hydraulic high reach single boom jumbo – offers high quality drilling in its most advanced form. Designed for fast and accurate drifting and production drilling of 12 to 125 m² (130 to 1345 sq-ft) cross sections, the 24-ton jumbo combines Sandvik’s novel technology, creativity and expertise, with extensive experience gained over many decades in the business. Being completely self-contained the DT912D is an optimal machine for multifaceted operations that will take excavation efficiency to another level.

Greater drilling power than ever before

The DT912D has ‘boosted performance’ written all over it. It features a 25 kW (33.5 Hp) high frequency RD525 rock drill for superior drilling performance and long lifetime. It also is equipped with the most powerful engine ever installed on a diesel-hydraulic jumbo, the Cummins Tier 4 Final with 205 kW (275 Hp). This means that the machine is able to bring a true boost to productivity with low fuel consumption. As standard, the jumbo has an electric controlled drilling system with added automatic functions, including one-hole automatics. It is also equipped with a SB150 universal boom for large, optimally shaped coverage and full automatic parallelism. In addition to face drilling, the versatile boom may also be used for crosscutting, bolt-hole drilling and extension drilling.

Completely self-contained for flexibility and speed of use

An efficient 4m³ (141 cfm) onboard compressor, together with an extra-large 1000 liter (265 gallon) water tank for air-mist flushing, enables the DT912D to operate independently from the tunnel or mine infrastructure thereby guaranteeing a longer drilling period from one set up. This enhances the efficiency of the total cycle time and gives extra flexibility of use. The DT912D offers rapid, safe and balanced tramming thanks to its powerful, 4-wheel-drive center articulated carrier. Also the ITA tunneling awards shortlisted FOPS/ROPS complied cabin, is ergonomically designed and well insulated to minimize noise and vibration; the noise level remaining under 73dB (A) at all times. As an option, the cabin is also available with a cabin lifting system delivering even better visibility for tramming and drilling. These features make the new jumbo a comfortable / user friendly workplace for the operator. Furthermore, the well-proven Sandvik Intelligent Control system Architecture (SICA), with comprehensive built-in diagnostics and user-friendly controls, ensures ease of use and maintenance.

Intelligent drilling

To ensure the best performance, the DT912D offers different instrumentation levels to choose from thereby optimizing its performance in accordance with specific needs. These include the silver package for drilling angles and depth monitoring, while the gold package offering semi-automatic drilling according to drill plan. The platinum package, being the most comprehensive one, has the advantage of automatic boom movements and drilling cycle. The gold and platinum packages are integrated with the Sandvik iSURE® tunnel management tool for accurate drilling, charging and blasting plans. In addition, iSURE® provides useful data collection and analysis reports for improving the work cycle and process. It may also be complemented with the new geoSURE rock mass analysis and visualization system.

| TECHNICAL SPECIFICATION IN BRIEF | SANDVIK DT912D |
| --- | --- |
| Coverage area | 14 000 x 10 000 mm / 125m² (46 ft x 33 ft / 1345 sq-ft) |
| Hydraulic rock drill | 1 x Sandvik RD525 (optional RD520) |
| Drill feed | 1 x Sandvik TF5i-16 feet |
| Boom | 1 x Sandvik SB150 (optional SB90) |
| Drilling control system | Sandvik SICA |
| Automation levels | Drilling and boom controls: one hole automatics (Silver, Gold and Platinum packages as options) |
| Hole length | up to 6 180 mm (up to 20 ft - 4 in) |
| Turning width (T-section) | 4 500 mm (14 ft – 9 in) |
| Tramming / drilling width | 2 500 mm / 3 000 mm (8.2 ft / 9.8 ft) |
| Tramming / drilling height | 3 590 mm* / 3 590 mm (11.8 ft / 11.8 ft) |
| Tramming length | 14 900 mm (48.9 ft) |
| Total weight | 24 000 kg (depending on options) (52,911 lbs or 26.45 tons) |

*   Minimum 3 190 mm (10.5 ft) with cabin lifting system.

For further information please contact:

Katri Miss
Marketing Communications Manager
Surface Drilling and Tunneling
Sandvik Construction
Office Phone: +358 205 44 4029
Mobile: +358 50 3609969
E-mail: katri.miss@sandvik.com

--------------------------------------------------------------------------------------------------------------------------------------------

Sandvik Group
Sandvik is a high-tech and global engineering group offering advanced products and services that enhance customer productivity, profitability and safety.  We have world - leading positions in selected areas - tools for metal cutting, equipment and tools for the mining and construction industries, stainless materials, special alloys, metallic and ceramic resistance materials as well as process systems. In 2014 the Group had about 47,000 employees and representation in approximately 130 countries, with sales of about 89,000 million SEK.

Sandvik Construction
Sandvik Construction is a business area within the Sandvik Group providing solutions for virtually any construction industry application encompassing such diverse businesses as surface rock quarrying, tunneling, excavation, demolition, road building, recycling and civil engineering. The range of products includes rock tools, drilling rigs, breakers, bulk-materials handling and crushing and screening machinery. In 2014 sales were about 9,000 million SEK, with approximately 3,000 employees.